## Slide 1: Unit – 1 Binary Systems and Logic Circuits
Hardik Doshi
 99789 11553
 hardik.doshi@darshan.ac.in
Digital Electronics (2131004) Darshan Institute of Engineering & Technology

## Slide 2: Topics to be covered
The Advantage of Binary
Number Systems
Use of Binary in Digital Systems
Logic Gates
Logic Family Terminology

## Slide 3: Advantages of Number System
Unit – 1: Review of Mathematical Theory Darshan Institute of Engineering & Technology

## Slide 5: Number Systems
Unit – 1: Binary Systems & Logic Circuits Darshan Institute of Engineering & Technology

## Slide 6: Common Number Systems
System | Base | Symbols | Used by Humans? | Used in Computers?
Decimal | 10 | 0, 1, … 9 | Yes | No
Binary | 2 | 0, 1 | No | Yes
Octal | 8 | 0, 1, … 7 | No | No
Hexa- decimal | 16 | 0, 1, … 9, A, B, … F | No | No

## Slide 7: Quantities / Counting
Decimal | Binary | Octal | Hexa- decimal
0 | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 10 | 2 | 2
3 | 11 | 3 | 3
4 | 100 | 4 | 4
5 | 101 | 5 | 5
6 | 110 | 6 | 6
7 | 111 | 7 | 7
Decimal | Binary | Octal | Hexa- decimal
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F

## Slide 8: Conversion among Bases
Possibilities
Example
Hexadecimal
Decimal
Octal
Binary
2510 = 110012 = 318 = 1916
Base

## Slide 9: Decimal to Binary
Technique
  Divide by two, keep track of the remainder
  First remainder is bit 0 (LSB, least-significant bit)
  Second remainder is bit 1 and so on
Decimal
Binary

## Slide 10: Example (Decimal to Binary)
12510 = ?2
2
125
1
2
62
0
2
31
1
2
15
1
2
7
1
2
3
1
2
1
1
0
12510 =
11111012

## Slide 11: Example (Decimal to Binary)
0.687510 = ?2
0.6875 x 2 =
1.3750
1
0.3750
+
0.3750 x 2 =
0.7500
0
0.7500
+
0.7500 x 2 =
1.5000
1
0.5000
+
0.5000 x 2 =
1.0000
1
0.0000
+
0.687510 =
0.10112
integer
fraction

## Slide 12: Exercise
(32)10 = ( )2
(555)10 = ( )2
(12999)10 = ( )2
(157.63)10 = ( )2
(64.125)10 = ( )2

## Slide 13: Binary to Decimal
Technique
  Multiply each bit by 2n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results
Binary
Decimal

## Slide 14: Example (Binary to Decimal)
1 0 1 0 1 1
1 x 20
1 x 21
0 x 22
1 x 23
0 x 24
1 x 25
+
+
+
+
+
1
2
0
1010112 =
0
32
+
+
+
+
+
4310
4310
8

## Slide 15: Example (Binary to Decimal)
1 1 . 1 1
1 x 20
1 x 21
+
1
2
11.112 =
+
3.7510
3.7510
1 x 2-2
1 x 2-1
+
0.25
0.5
+
+
+

## Slide 16: Exercise
(11011)2 = ( )10
(101101)2 = ( )10
(11101111)2 = ( )10
(110.011)2 = ( )10
(1001.0010)2 = ( )10

## Slide 17: Decimal to Octal
Technique
  Divide by eight
  Keep track of the remainder
Decimal
Octal

## Slide 18: Example (Decimal to Octal)
12510 = ?8
8
125
5
8
15
7
8
1
1
0
12510 =
1758

## Slide 19: Example (Decimal to Octal)
0.687510 = ?8
0.6875 x 8 =
5.5000
5
0.5000
+
0.5000 x 8 =
4.0000
4
0.0000
+
0.687510 =
0.548
integer
fraction

## Slide 20: Exercise
(32)10 = ( )8
(555)10 = ( )8
(12999)10 = ( )8
(157.63)10 = ( )8
(64.125)10 = ( )8

## Slide 21: Octal to Decimal
Technique
  Multiply each bit by 8n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results
Octal
Decimal

## Slide 22: Example (Octal to Decimal)
7 2 4
4 x 80
2 x 81
7 x 82
+
+
7248 =
46810
46810
4
16
448
+
+

## Slide 23: Example (Octal to Decimal)
4 3 . 2 5
3 x 80
4 x 81
+
3
32
43.252 =
+
35.328110
35.328110
5 x 8-2
2 x 8-1
+
0.0781
0.25
+
+
+

## Slide 24: Exercise
(32)8 = ( )10
(555)8 = ( )10
(12333)8 = ( )10
(157.63)8 = ( )10
(64.125)8 = ( )10

## Slide 25: Decimal to Hexa-Decimal
Technique
  Divide by 16
  Keep track of the remainder
Decimal
Hexa-Decimal

## Slide 26: Example (Decimal to HexaDecimal)
123410 = ?16
16
1234
2
123410 =
4D216
16
77
13=D
16
4
4
0

## Slide 27: Exercise
(32)10 = ( )16
(555)10 = ( )16
(12999)10 = ( )16
(157.63)10 = ( )16
(64.125)10 = ( )16

## Slide 28: Hexa-Decimal to Decimal
Technique
  Multiply each bit by 16n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results
Hexa-Decimal
Decimal

## Slide 29: Example (HexaDecimal to Decimal)
A B C
C x 160
B x 161
A x 162
+
+
ABC16 =
274810
274810
12 x 160
11 x 161
10 x 162
+
+
12
176
2560
+
+

## Slide 30: Exercise
(FA8)16 = ( )10
(9AC3)16 = ( )10
(1A74D)16 = ( )10
(1AC.9A)16 = ( )10
(ABC.5AC)16 = ( )10

## Slide 31: Octal to Binary
Technique
  Convert each octal digit to a 3-bit equivalent binary representation
Octal
Binary

## Slide 32: Example (Octal to Binary)
7058 = ?2
7 0 5
101
000
111
7058 =
1110001012

## Slide 33: Exercise
(463)8 = ( )2
(2056)8 = ( )2
(2057.64)8 = ( )2
(6543.04)8 = ( )2
(7476.47)8 = ( )2

## Slide 34: Binary to Octal
Technique
  Group bits in threes, starting on right
  Convert to octal digits
Binary
Octal

## Slide 35: Example (Binary to Octal)
10110101112 = ?8
1
011
001
10110101112 =
13278
111
010
3
2
7

## Slide 36: Exercise
(11011)2 = ( )8
(101101)2 = ( )8
(11101111)2 = ( )8
(110.011)2 = ( )8
(1001.0010)2 = ( )8

## Slide 37: Hexa-Decimal to Binary
Technique
  Convert each hexadecimal digit to a 4-bit equivalent binary representation
Hexa-Decimal
Binary

## Slide 38: Example (Hexa-Decimal to Binary)
10AF16 = ?2
1 0 A F
1111
1010
0000
10AF16 =
10000101011112
0001

## Slide 39: Exercise
(FA8)16 = ( )2
(9AC3)16 = ( )2
(1A74D)16 = ( )2
(1AC.9A)16 = ( )2
(ABC.5AC)16 = ( )2

## Slide 40: Binary to Hexa-Decimal
Technique
  Group bits in fours, starting on right
  Convert to hexadecimal digits
Binary
Hexa-Decimal

## Slide 41: Example (Binary to Hexa-Decimal)
10110101112 = ?16
0010
10110101112 =
2D716
0111
1101
2
D
7

## Slide 42: Exercise
(11011)2 = ( )16
(101101)2 = ( )16
(11101111)2 = ( )16
(110.011)2 = ( )16
(1001.0010)2 = ( )16

## Slide 43: Octal to Hexa-Decimal
Technique
  Convert Octal to Binary
  Regroup bits in fours from right
  Convert Binary to Hexa-Decimal
Octal
Hexa-Decimal

## Slide 44: Example (Octal to Hexa-Decimal)
10768 = ?16
1 0 7 6
110
111
000
10768 =
23E16
001
1110
0011
0010
E
3
2

## Slide 45: Exercise
(463)8 = ( )16
(2056)8 = ( )16
(2057.64)8 = ( )16
(6543.04)8 = ( )16
(7476.47)8 = ( )16

## Slide 46: Hexa-Decimal to Octal
Technique
  Convert Hexa-Decimal to Binary
  Regroup bits in three from right
  Convert Binary to Octal
Hexa-Decimal
Octal

## Slide 47: Example (Hexa-Decimal to Octal)
1F0C16 = ?8
1 F 0 C
1100
0000
1111
1F0C16 =
174148
0001
100
001
100
4
1
4
111
7
001
1
000
0

## Slide 48: Exercise
(FA8)16 = ( )8
(9AC3)16 = ( )8
(1A74D)16 = ( )8
(1AC.9A)16 = ( )8
(ABC.5AC)16 = ( )8

## Slide 49: Accuracy in Binary Number Conversion
Convert (0.252)10 to binary with an error less than 1%.
Solution
Absolute value of allowable error is found by calculating 1% of the number
Maximum error due to truncation is set to be less than allowable error by solving from . This equation is written as
Inverting both sides of the inequality

## Slide 50: Accuracy in Binary Number Conversion
Taking log of both sides and solving for
This indicates that the use of 9 bits in the binary number will guarantee an error less than 1%.
So the conversion is carried out to 9 places which results in

## Slide 51: 9’s Complement
9’s complement of a decimal number is obtained by subtracting each digit of that decimal number from 9.
Example
9
9
9
9
3
4
6
5
6
5
3
4
-
(9’s complement of 3465)
9
9
9
.
7
8
2
.
2
1
7
.
-
(9’s complement of 782.54)
9
9
5
4
4
5

## Slide 52: 10’s Complement
10’s complement of a decimal number is obtained by adding 1 to its 9’s complement.
Example
9
9
9
9
3
4
6
5
6
5
3
4
-
(10’s complement of 3465)
2
1
7
.
-
(10’s complement of 782.54)
9
9
9
.
9
9
7
8
2
.
5
4
4
5
1
6
5
3
5
1
+
+
2
1
7
4
6
.

## Slide 53: Subtraction using 9’s complement
Obtain 9’s complement of subtrahend
Add the result to minuend and call it intermediate result
If carry is generated then answer is positive and add the carry to Least Significant Digit (LSD)
If there is no carry then answer is negative and take 9’s complement of intermediate result and place negative sign to the result

## Slide 54: Example
7
4
5
.
4
3
6
.
-
8
1
6
2
1) 745.81 – 436.62
7
4
5
.
8
1
5
6
3
.
+
3
7
3
0
9
.
1
1
8
+
1
3
0
9
.
1
9
3
0
9
.
1
9
9’s complement

## Slide 55: Example
7
4
5
.
4
3
6
.
-
8
1
6
2
2) 436.62 - 745.81
2
5
4
.
+
1
8
6
9
0
.
8
0
3
0
9
.
1
9
3
0
9
.
1
9
-
4
3
6
.
6
2
-
9’s complement
9’s complement
As carry is not generated, so take 9’s complement of the intermediate result and add ‘ – ‘ sign to the result

## Slide 56: Subtraction using 10’s complement
Obtain 10’s complement of subtrahend
Add the result to minuend
If carry is generated then ignore it and result itself is answer
If there is no carry then answer is negative and take 10’s complement of result and place negative sign to the result

## Slide 57: Example
7
4
5
.
4
3
6
.
-
8
1
6
2
1) 745.81 – 436.62
5
6
3
.
+
7
4
5
.
8
1
3
8
3
0
9
.
1
1
9
3
0
9
.
1
9
Ignore the carry
10’s complement

## Slide 58: Example
7
4
5
.
4
3
6
.
-
8
1
6
2
2) 436.62 - 745.81
2
5
4
.
+
1
9
6
9
0
.
8
1
3
0
9
.
1
9
3
0
9
.
1
9
-
4
3
6
.
6
2
-
10’s complement
10’s complement
As carry is not generated, so take 10’s complement of the intermediate result and add ‘ – ‘ sign to the result

## Slide 59: Binary Addition
Rules for binary addition
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 10 i.e. 0 with a carry of 1
1
1
0
1
0
1
1
1
0
1
0
1
1
1
1
1
1
+
.
1
0
1
.
0
1
1
.
0
0
0
1
1

## Slide 60: Binary Subtraction
Rules for binary subtraction
0 - 0 = 0
1 – 1 = 0
1 – 0 = 1
0 – 1 = 1, with a borrow 1
1
0
1
0
0
1
1
1
0
0
1
0
-
.
0
1
0
.
1
1
1
.
0
1
1
1
0
1
1
1
0
1
1
0

## Slide 61: Binary Multiplication
1 0 1 1 1
1 0 0 1 1
x
1
1
1
0
1
1
1
1
0
1
0
0
0
0
0
0
0
0
0
0
1
1
1
0
1
1
0
1
0
1
1
0
1
1

## Slide 62: Binary Division
1 0 1 1 0 1
110
0
0 0 0
1 0 1
1
1 1 0
1 0 1
0
1 1 0
1 0 0
1
1 1 0
1 1
1
1
1
.
1
0
1 1 0
0 0 0

## Slide 63: 1’s Complement
1’s complement of a binary number is obtained by subtracting each digit of that binary number from 1.
Example
1
1
1
1
1
1
0
1
0
0
1
0
-
(1’s complement of 1101)
1
1
1
.
1
0
1
.
0
1
0
.
-
(1’s complement of 101.01)
1
1
0
1
1
0

## Slide 64: 2’s Complement
2’s complement of a binary number is obtained by adding 1 to its 1’s complement.
Example
1
1
1
1
1
1
0
0
0
0
1
1
-
(2’s complement of 1100)
0
1
0
.
-
(2’s complement of 101.01)
1
1
1
.
1
1
1
0
1
.
0
1
1
0
1
0
1
0
0
1
+
+
0
1
0
1
1
.

## Slide 65: Subtraction using 1’s Complement

## Slide 66: Subtraction using 2’s Complement

## Slide 67: Exercise
Express -45 in 8-bit 2’s complement form.
Express -73.75 in 12 bit 2’s complement form.

## Slide 68: Binary Codes
Unit – 1: Binary Systems & Logic Circuits Darshan Institute of Engineering & Technology

## Slide 69: 8421 BCD Code (Natural BCD Code)
Each decimal digit, 0 through 9, is coded by 4-bit binary number
8, 4, 2 and 1 weights are attached to each bit
BCD code is weighted code
1010, 1011, 1100, 1101, 1110 and 1111 are illegal codes
Less efficient than pure binary
Arithmetic operations are more complex than in pure binary
Example
1 4
0100
0001
Decimal
BCD
Binary
1110

## Slide 70: Binary Codes
Decimal | Binary | BCD
0 | 0 | 0000
1 | 1 | 0001
2 | 10 | 0010
3 | 11 | 0011
4 | 100 | 0100
5 | 101 | 0101
6 | 110 | 0110
7 | 111 | 0111
Decimal | Binary | BCD
8 | 1000 | 1000
9 | 1001 | 1001
10 | 1010 | 0001 0000
11 | 1011 | 0001 0001
12 | 1100 | 0001 0010
13 | 1101 | 0001 0011
14 | 1110 | 0001 0100
15 | 1111 | 0001 0101

## Slide 71: BCD Addition
0
0
1
0
0
0
0
1
0
0
1
1
+
0
1
0
1
0
0
1
1
1
0
0
0
2
5
1
3
+
3
8
No carry, no illegal code. So, this is the correct sum.

## Slide 72: BCD Addition
0110
0111
1001
+
.0110
679.6
536.8
+
1216.4
All are illegal codes
0101
0011
0110
.1000
1011
1010
1111
.1110
+0110
+0110
+0110
+.0110
10001
10000
10101
1.0100
1
+
1
+
1
+
1
+
0010
0001
0110
.0100
0001
Add 0110 to each
Propagate carry
Corrected Sum

## Slide 73: BCD Subtraction
0
0
1
1
0
0
0
1
0
0
1
0
-
1
0
0
0
0
1
0
1
0
0
1
1
3
8
1
5
-
2
3
No borrow. So, this is the correct difference.

## Slide 74: BCD Subtraction
0010
0000
0110
-
.0111
206.7
147.8
-
58.9
Borrows are present
0001
0100
0111
.1000
0000
1011
1110
.1111
-0110
-0110
-.0110
0101
1000
.1001
Subtract 0110
Corrected difference

## Slide 75: Excess Three (XS-3) Code
Excess Three Code = 8421 BCD + 0011(3)
XS-3 code is non-weighted BCD code
Also known as self complementing code
0000, 0001, 0010, 1101, 1110 and 1111 are illegal codes
Example
1 4
0100
0001
Decimal
BCD
XS-3
0100
0111

## Slide 76: XS-3 Addition
0
1
1
0
0
1
0
1
1
0
1
1
+
1
0
1
0
1
0
1
1
0
1
0
1
3
7
2
8
+
6
5
Propagate carry to next group
1
1
+
0
1
0
1
1
1
0
0
0
0
1
1
+
0
0
1
1
-
1
0
0
0
1
0
0
1
Add 0011 to group which generated carry
Subtract 0011 to group which do not generated carry

## Slide 77: XS-3 Addition
0101
0111
1010
+
.1001
247.6
359.4
+
607.0
Carry generated
0110
1000
1100
.0111
1011
1111
10110
1.0000
- 0011
+0011
+0011
+.0011
1011
10000
0111
.0000
1
+
1
+
1
+
Propagate carry
.0000
0111
0000
1100
Add 0011 to group which generated carry
Subtract 0011 to group which do not generated carry
Corrected Sum in XS-3
.0011
1010
0011
1001

## Slide 78: XS-3 Subtraction
0101
1001
1010
-
267
175
-
092
0100
1010
1000
0000
1111
0010
-0011
+0011
0011
1100
0101
Subtract 0011 to group which generated borrow
Add 0011 to group which do not generated borrow
+0011

## Slide 79: XS-3 Subtraction
1000
1010
.1001
-
57.6
27.8
-
29.8
0101
1010
.1011
0010
1111
.1110
-0011
+0011
0101
1100
.1011
Subtract 0011 to group which generated borrow
Add 0011 to group which do not generated borrow
-.0011

## Slide 80: Gray Code
Only one bit changes between each pair of successive code words (Unit distance code).
Gray code is a reflected code.
Gray codes are designed recursively using following rules:
  1-bit Gray code has two code words, 0 and 1.
  The first 2n code words of an (n+1)-bit Gray code equal the code words of n-bit gray code, written in order with a leading 0 appended.
  The last 2n code words of an (n+1)-bit Gray code equal the code words of n-bit gray code, but written in reverse order with a leading 1 appended.

## Slide 81
Gray Code |  |  |  | Decimal | 4-bit Binary
1-bit | 2-bit | 3-bit | 4-bit |  | 
0 | 0 0 | 0 0 0 | 0 0 0 0 | 0 | 0000
1 | 0 1 | 0 0 1 | 0 0 0 1 | 1 | 0001
 | 1 1 | 0 1 1 | 0 0 1 1 | 2 | 0010
 | 1 0 | 0 1 0 | 0 0 1 0 | 3 | 0011
 |  | 1 1 0 | 0 1 1 0 | 4 | 0100
 |  | 1 1 1 | 0 1 1 1 | 5 | 0101
 |  | 1 0 1 | 0 1 0 1 | 6 | 0110
 |  | 1 0 0 | 0 1 0 0 | 7 | 0111
 |  |  | 1 1 0 0 | 8 | 1000
 |  |  | 1 1 0 1 | 9 | 1001
 |  |  | 1 1 1 1 | 10 | 1010
 |  |  | 1 1 1 0 | 11 | 1011
 |  |  | 1 0 1 0 | 12 | 1100
 |  |  | 1 0 1 1 | 13 | 1101
 |  |  | 1 0 0 1 | 14 | 1110
 |  |  | 1 0 0 0 | 15 | 1111

## Slide 82: Binary to Gray Conversion
Conversion of n-bit Binary number (B) to Gray Code (G) is as follows:
Example: Convert (1001)2 to Gray Code.
1
Binary
Gray
0
0
1
1
1
0
1

## Slide 83: Gray to Binary Conversion
Conversion of n-bit Gray Code (G) to Binary Number (B) is as follows:
Example: Convert Gray code 1101 to Binary.
1
Gray
Binary
1
0
1
1
0
0
1

## Slide 84: Logic Gates
Most basic logical unit of the digital system is gate circuit
Types of gate circuits are as follows
  AND Gate
  OR Gate
  NOT Gate (Inverter)
  NOR Gate
  NAND Gate
  XOR Gate
  XNOR Gate

## Slide 85: 1. AND Gate
AND Gate has an output which is normally at logic level “0” and only goes “HIGH” to a logic level “1” when ALL of its inputs are at logic level “1”
A
B
C
Logic Notation
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Truth Table
2-input AND Gate

## Slide 86: 2. OR Gate
OR Gate or Inclusive-OR gate has an output which is normally at logic level “0” and only goes “HIGH” to a logic level “1” when one or more of its inputs are at logic level “1”.
A
B
C
Logic Notation
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Truth Table
2-input OR Gate

## Slide 87: 3. NOT (Inverter) Gate
NOT gate has an output which is always opposite to input level.
A
C
Logic Notation
A | C
0 | 1
1 | 0
Truth Table
Inverter Gate

## Slide 88: 4. NOR Gate
NOR Gate is an OR gate followed by an inverter.
A
B
C
Logic Notation
A | B | C
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Truth Table
2-input NOR Gate

## Slide 89: 5. NAND Gate
NAND Gate is an AND gate followed by an inverter.
A
B
C
Logic Notation
A | B | C
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Truth Table
2-input NAND Gate

## Slide 90: 6. Exclusive-OR (X-OR) Gate
X-OR gate that has 1 state when one and only one of its two inputs assumes a logic 1 state and has 0 state when all of its input are same.
Also known as anti-coincidence gate or inequality detector.
A
B
C
Logic Notation
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Truth Table
2-input XOR Gate

## Slide 91: 7. Exclusive-NOR (X-NOR) Gate
X-NOR gate that has 1 state when all of its input are same and has 0 state when one of its input has 0 state and other input is 1 state.
Also known as equality detector.
A
B
C
Logic Notation
A | B | C
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Truth Table
2-input XNOR Gate

## Slide 92: NAND as Universal Gate
NOT using NAND
A
A’
A
B
(AB)’
((AB)’)’ = AB
AND using NAND
A
B
A’
(A’B’)’ = (A+B)
OR using NAND
B’

## Slide 93: NOR as Universal Gate
NOT using NOR
A
A’
A
B
(A+B)’
((A+B)’)’ = A+B
OR using NOR
A
B
A’
(A’+B’)’ = AB
AND using NOR
B’